## Slide 1
EE499 SENIOR DESIGN PROJECT
Report 1 — Problem & Design Requirements
Smart Home
Energy Management
with Priority-Based Load Control
TEAM 16 · PME
ADVISOR & CUSTOMER
Dr. Fahd Hariri
Electrical and Computer Engineering
King Abdulaziz University · Fall 2026
Notes: ⏱ 0:30
Opening slide: the tower spells our names and university IDs while we introduce the project — Smart Home Energy Management with Priority-Based Load Control, Report 1, advisor Dr. Fahd Hariri.

## Slide 2
EE499 · Team 16 · Smart Home Energy Management
2
AGENDA
What we will cover
Introduction
01
Problem Statement
02
Objectives
03
Design Requirements
04
Notes: ⏱ 0:10
Four parts: introduction, problem statement, objectives, design requirements.

## Slide 3
01
Introduction
Why household energy needs managing
01
02
03
04
Notes: ⏱ 0:05
Why household energy needs managing.

## Slide 4
EE499 · Team 16 · Smart Home Energy Management
4
01 · INTRODUCTION
Where household electricity goes
47 %
of Saudi electricity → homes
Residential share of national consumption
≈ 70 %
of home electricity → air-conditioning
Highest share worldwide
+67 %
per extra kWh above 6,000 kWh / month
18 → 30 halalas / kWh
Notes: ⏱ 0:35
Homes take 47 % of Saudi electricity; about 70 % of home electricity goes to air-conditioning; above 6,000 kWh/month every extra kWh costs 67 % more (18 → 30 halalas).

## Slide 5
EE499 · Team 16 · Smart Home Energy Management
5
01 · INTRODUCTION
What the single total hides
14 %
median electricity saved
with real-time, per-appliance feedback
5–15 %
extra AC energy from a dirty filter
Hidden in the total — visible per appliance
≈ 53
house fires / day in KSA
#1 cause: electrical incidents
14 %: ACEEE meta-review, 57 studies (2010) — an indication, not a promise. · 5–15 %: U.S. DOE, Energy Saver, “Maintaining your air conditioner”.
53 / day: 193,437 house fires in 10 years (Civil Defense via Arab News, 2015) ÷ 3,650 days.
Notes: ⏱ 0:35
Per-appliance feedback saved a median 14 % (ACEEE, 57 studies). A dirty AC filter wastes 5–15 % and stays hidden in the total. About 53 house fires a day in KSA, mostly electrical.

## Slide 6
EE499 · Team 16 · Smart Home Energy Management
6
01 · INTRODUCTION
One meter. One number.
TOTAL
kWh
?
Air conditioner
?
Refrigerator
?
Water heater
?
Washing machine
Not a luxury. A need.
Cost
Which appliance? → see the bill, stay in budget
Continuity
Which can wait? → essentials stay ON
Safety
Which misbehaves? → warn early, fail safe
Notes: ⏱ 0:30
A conventional meter gives one number. Three questions it cannot answer — which appliance, which can wait, which misbehaves — map to cost, continuity and safety. Not a luxury: a need.

## Slide 7
EE499 · Team 16 · Smart Home Energy Management
01 · INTRODUCTION
From one total to per-appliance visibility
Conventional meter
Whole-house total only
Per-appliance monitoring
Air conditioner
Refrigerator
Water heater
Washing machine
MEASURED FOR EACH APPLIANCE
– Voltage (V) and current (I)
– Power (P) and energy (kWh)
– ON / OFF status
7
Notes: ⏱ 0:25
Our system measures each appliance separately: voltage, current, power, energy and ON/OFF status.

## Slide 8
EE499 · Team 16 · Smart Home Energy Management
8
01 · INTRODUCTION
Priority-based load management
Grid supply
fixed limit
Smart controller
compares demand
User sets
priorities
Refrigerator
P1 · highest
ON
Air conditioner
P2
ON
Water heater
P3
SHED
Washing machine
P4 · lowest
SHED
Simplified from the demand-side management concept in [4].
1
User sets priorities
2
Demand > limit → shed lowest
3
Essentials stay ON
Notes: ⏱ 0:30
User sets priorities; when demand exceeds the limit the lowest-priority load is shed; essentials stay on.

## Slide 9
EE499 · Team 16 · Smart Home Energy Management
9
01 · INTRODUCTION
Abnormal operation — a supporting function
Deviation from baseline
User warning
Supports — not replaces — control
EVIDENCE
Whole-house estimate
less reliable
Direct sub-metering
more reliable
Anomaly detection on appliance data — Rashid et al., Applied Energy, 2019.
Notes: ⏱ 0:25
Abnormal operation is a supporting function: deviation from the appliance’s own baseline triggers a warning. Direct sub-metering is more reliable than whole-house estimates.

## Slide 10
02
Problem Statement
The engineering need
01
02
03
04
Notes: ⏱ 0:05
Problem statement.

## Slide 11
EE499 · Team 16 · Smart Home Energy Management
11
02 · PROBLEM STATEMENT
What households face today
No per-appliance visibility
Heavy-demand loads may run at the same time
Costs rise unnoticed
Essentials not prioritised
Abnormal behaviour hidden
Notes: ⏱ 0:25
Five problems households face today.

## Slide 12
EE499 · Team 16 · Smart Home Energy Management
12
02 · PROBLEM STATEMENT
Two core problems
Limited visibility of energy & cost
Conventional meters report only total household energy, making it hard to track individual appliances or spot abnormal behaviour.
Lack of priority-based load control
High-demand appliances run at the same time without real-time tracking, and essential loads are not prioritised when power is limited.
Notes: ⏱ 0:25
Two core problems: limited visibility of energy and cost, and no priority-based load control.

## Slide 13
EE499 · Team 16 · Smart Home Energy Management
13
02 · PROBLEM STATEMENT
Problem statement
There is a need for a residential energy-management approach that provides ① appliance-level monitoring, supports ② priority-based control of connected loads, and helps users ③ manage electricity consumption and cost while ④ maintaining supply to essential loads.
①
Appliance-level monitoring
②
Priority-based load control
③
Consumption & cost management
④
Essential loads kept supplied
Notes: ⏱ 0:20
The need: residential energy management with monitoring, priority control, cost management and supplied essentials.

## Slide 14
03
Objectives
Higher-level goals · lower-level behaviours
01
02
03
04
Notes: ⏱ 0:05
Objectives.

## Slide 15
EE499 · Team 16 · Smart Home Energy Management
15
03 · OBJECTIVES
Higher-level objectives
HLO-1
Economic
Lower consumption
Lower cost
HLO-2
Reliability
Essentials stay
supplied
HLO-3
Safety & efficiency
Safer operation
Efficient use
Notes: ⏱ 0:25
Three higher-level objectives: economic, reliability, safety and efficiency.

## Slide 16
EE499 · Team 16 · Smart Home Energy Management
16
03 · OBJECTIVES
Lower-level objectives
LLO-1
Monitor
Each load + total
LLO-2
Detect
Abnormal → warn
LLO-3
Prioritise
Shed lowest above limit
LLO-4
Budget
Energy & cost vs. budget
LLO-5
Inform
Status · cost · warnings
LLO-6
Stay safe
Fail-safe · override
Notes: ⏱ 0:30
Six lower-level objectives: monitor, detect, prioritise, budget, inform, stay safe.

## Slide 17
04
Design Requirements
Specs · constraints · standards · assumptions · deliverables
01
02
03
04
Notes: ⏱ 0:05
Design requirements.

## Slide 18
EE499 · Team 16 · Smart Home Energy Management
18
04 · DESIGN REQUIREMENTS
Design specifications (1/2)
DS-01
Accuracy
±5 %
V · I · P · energy
→ LLO-1
DS-02
Update rate
≤ 3 s
Readings + status
→ LLO-1 · 5
DS-03
Abnormal detection
120 / 80 %
of baseline · ≥ 5 s
≥ 90 % detected
→ LLO-2
DS-04
Load control
≤ 1 s
≥ 4 channels · ≥ 3 levels
→ LLO-3
Notes: ⏱ 0:30
DS-01 to DS-04: ±5 % accuracy, ≤ 3 s updates, ≥ 90 % abnormal detection, ≤ 1 s load control.

## Slide 19
EE499 · Team 16 · Smart Home Energy Management
19
04 · DESIGN REQUIREMENTS
Design specifications (2/2)
DS-05
Reconnection
5 s
Stable margin · highest first
→ LLO-3 · 6
DS-06
Cost & budget
±5 %
cost-estimate error
alerts: 50 · 80 · 100 %
→ LLO-4
DS-07
User warnings
≤ 5 s
7-day log · 1 h
→ LLO-2 · 5
DS-08
Fail-safe
≤ 2 s
De-energize · override
→ LLO-6
Notes: ⏱ 0:30
DS-05 to DS-08: reconnection, cost and budget alerts, user warnings, ≤ 2 s fail-safe.

## Slide 20
REQUIRED BEHAVIOUR · DS-03 / DS-07
Abnormal-operation warning
120 / 80 %
of baseline
≥ 5 s
persistence
≥ 90 %
detection rate
≤ 5 s
to warn
Notes: ⏱ 0:25
The warning behaviour: outside 120 / 80 % of baseline for ≥ 5 s → warn within 5 s.

## Slide 21
EE499 · Team 16 · Smart Home Energy Management
21
04 · DESIGN REQUIREMENTS
Realistic constraints
C-01 · BUDGET
≤ 1,000 SAR
C-04 · SCHEDULE
Before the deadline
C-02 · SCOPE
Single-phase
C-03 · LAB POWER
≤ 2 kW
C-05 · APPLIANCES
No modification
C-06 · SAFETY
Supervised lab
Notes: ⏱ 0:20
Constraints C-01 to C-06: budget, single-phase scope, lab power, schedule, no appliance modification, supervised lab.

## Slide 22
EE499 · Team 16 · Smart Home Energy Management
22
04 · DESIGN REQUIREMENTS
Engineering standards
IEC
IEC 60730-1:2022
Automatic controls
IEC
IEC 62053-21:2020
Energy-metering accuracy
SBC
SBC 401 (2024)
Wiring & protection
GSO
Gulf Technical Regulation
Low-voltage equipment
Engineering and safety guidance — certification out of scope.
Notes: ⏱ 0:20
Standards we follow for guidance: IEC 60730-1, IEC 62053-21, SBC 401, GSO low-voltage regulation.

## Slide 23
EE499 · Team 16 · Smart Home Energy Management
23
04 · DESIGN REQUIREMENTS
Realistic assumptions
Normal operation at baseline
Test loads available
Lab + calibrated instruments
Protected, grounded supply
Up-to-date tariff
Correct user inputs
Notes: ⏱ 0:20
Assumptions behind the design.

## Slide 24
EE499 · Team 16 · Smart Home Energy Management
24
04 · DESIGN REQUIREMENTS
Project deliverables
D-1
Prototype
D-2
Test bench
D-3
Firmware & UI
D-4
Validation results
D-5
Documentation
Notes: ⏱ 0:20
Five deliverables: prototype, test bench, firmware and UI, validation results, documentation.

## Slide 25
EE499 · TEAM 16
Thank you —
questions?
Visibility. Priority. Safety.
A need — not a luxury.
Team 16
Ali Khudhayr
Mohammad Kassem
Omar Baflah
PRIORITY CONTROL IN ACTION · DS-04 / DS-05
≤ 1 s
shedding starts
≥ 4 · ≥ 3
channels · priorities
5 s
stable margin
3 s
motor restarts
Notes: ⏱ 0:15
Close. The summary and the priority-control demo loop on their own during questions.

## Slide 26
[1] M. Aldubyan, “Future of residential electricity demand in Saudi Arabia and the role of energy efficiency in 2060’s net zero pledge,” Development and Sustainability in Economics and Finance, vol. 8, p. 100086, Dec. 2025.
[2] N. Howarth et al., “Staying cool in a warming climate: Temperature, electricity and air conditioning in Saudi Arabia,” Climate, vol. 8, no. 1, p. 4, Jan. 2020.
[3] Saudi Electricity Regulatory Authority (SERA), “Consumption tariff.” [Online]. Available: sera.gov.sa. Accessed 29 Sep. 2026.
[4] S. Panda et al., “Priority-based scheduling in residential energy management systems integrated with renewable sources using adaptive Salp swarm algorithm,” Results in Engineering, vol. 23, p. 102643, Sep. 2024.
[5] H. Rashid, P. Singh, V. Stankovic and L. Stankovic, “Can non-intrusive load monitoring be used for identifying an appliance’s anomalous behaviour?,” Applied Energy, vol. 238, pp. 796–805, Mar. 2019.
References
SOURCES