## Slide 1
EE499 SENIOR DESIGN PROJECT
Report 1 — Problem & Design Requirements
Smart Home Energy Management
with Priority-Based Load Control
TEAM 16
Ali Khudhayr 2343192 · PME
Mohammad Kassem 2364954 · PME
Omar Baflah 2343198 · PME
ADVISOR & CUSTOMER
Dr. Fahd Hariri
Electrical and Computer Engineering
King Abdulaziz University · Fall 2026

## Slide 2
EE499 · Team 16 · Smart Home Energy Management
1
AGENDA
What we will cover
Introduction
01
Problem Statement
02
Objectives
03
Design Requirements
04

## Slide 3
01
Introduction
Why household energy needs managing
01
02
03
04

## Slide 4
EE499 · TEAM 16
of Saudi electricity → homes
Residential share of national consumption

## Slide 5
INSIDE THE HOME
about
of home electricity
→ air-conditioning
Highest share worldwide
HOUSEHOLD ELECTRICITY
≈30 %
other uses
≈70 %
air-conditioning
من سلايد 4 الى 9 ادمج في سلايدين

## Slide 6
THE TARIFF
Above 6,000 kWh / month
per extra kWh
18 → 30 halalas / kWh
18
≤ 6,000 kWh
30
> 6,000 kWh

## Slide 7
THE COST OF NOT SEEING
median
electricity saved
with real-time, per-appliance feedback
WHAT WORKED
Real-time
Per appliance
Energy + cost
ACEEE meta-review, 57 studies (2010) · many small and short — an indication, not a promise.

## Slide 8
HIDDEN WASTE
a dirty AC filter costs
5–15 %
extra AC energy
Neglect → energy use steadily rises
WHERE IT SHOWS
Total: hidden
Per appliance: visible
vs. its own baseline
U.S. Department of Energy, Energy Saver: “Maintaining your air conditioner”.
شوف حريري
هل نقدر نحط معلومة جديدة ما استخدمنا رفرنسها

## Slide 9
SAFETY AT HOME
about
house fires / day in KSA
#1 cause: electrical incidents
2018 · HOUSE FIRES
90 deaths
1,364 injuries
Fire detection: out of scope (C-03)
193,437 house fires in 10 years (Civil Defense via Arab News, 2015) ÷ 3,650 days ≈ 53 per day.

## Slide 10
One meter. One number.
TOTAL
kWh
?
Air conditioner
?
Refrigerator
?
Water heater
?
Washing machine
Which appliance?
Which can wait?
Which misbehaves?
ادمج 10و 11
واختصر

## Slide 11
Not a luxury. A need.
Cost
See the bill
Stay in budget
Continuity
Essentials stay ON
when demand is limited
Safety
Warn early
Fail safe

## Slide 12
EE499 · Team 16 · Smart Home Energy Management
12
01 · INTRODUCTION
From one total to per-appliance visibility
Conventional meter
Total only
Per-appliance monitoring
Air conditioner
V · I · P · kWh · ON/OFF
Refrigerator
V · I · P · kWh · ON/OFF
Water heater
V · I · P · kWh · ON/OFF
Washing machine
V · I · P · kWh · ON/OFF
وضح واعد الصياغة حط شرطات
اختصر لا تكرر ال v I p kwh on off

## Slide 13
EE499 · Team 16 · Smart Home Energy Management
13
01 · INTRODUCTION
Priority-based load management
Demand-side management concept. Reproduced from [4].
1
User sets priorities
2
Demand > limit → shed lowest
3
Essentials stay ON

## Slide 14
EE499 · Team 16 · Smart Home Energy Management
14
01 · INTRODUCTION
Abnormal operation — a supporting function
Deviation from baseline
User warning
Supports — not replaces — control
EVIDENCE
Whole-house estimate
less reliable
Direct sub-metering
more reliable
Anomaly detection on appliance data — Rashid et al., Applied Energy, 2019.

## Slide 15
02
Problem Statement
The engineering need
01
02
03
04

## Slide 16
EE499 · Team 16 · Smart Home Energy Management
16
02 · PROBLEM STATEMENT
What households face today
No per-appliance visibility
Heavy loads overlap
Costs rise unnoticed
Essentials not prioritised
Abnormal behaviour hidden

## Slide 17
EE499 · Team 16 · Smart Home Energy Management
17
02 · PROBLEM STATEMENT — RESIDENTIAL ENERGY MANAGEMENT WITH
The need
Appliance-level monitoring
Priority-based load control
Consumption & cost management
Essential loads kept supplied

## Slide 18
03
Objectives
Higher-level goals · lower-level behaviours
01
02
03
04

## Slide 19
EE499 · Team 16 · Smart Home Energy Management
19
03 · OBJECTIVES
Higher-level objectives
HLO-1
Economic
Lower consumption
Lower cost
HLO-2
Reliability
Essentials stay
supplied
HLO-3
Safety & efficiency
Safer operation
Efficient use

## Slide 20
EE499 · Team 16 · Smart Home Energy Management
20
03 · OBJECTIVES
Lower-level objectives
LLO-1
Monitor
Each load + total
LLO-2
Detect
Abnormal → warn
LLO-3
Prioritise
Shed lowest above limit
LLO-4
Budget
Energy & cost vs. budget
LLO-5
Inform
Status · cost · warnings
LLO-6
Stay safe
Fail-safe · override

## Slide 21
04
Design Requirements
Specs · constraints · standards · assumptions · deliverables
01
02
03
04

## Slide 22
EE499 · Team 16 · Smart Home Energy Management
25
04 · DESIGN REQUIREMENTS
Design specifications (1/2)
DS-01
Accuracy
±5 %
V · I · P · energy
→ LLO-1
DS-02
Update rate
≤ 3 s
Readings + status
→ LLO-1 · 5
DS-03
Abnormal detection
≥ 90 %
120 / 80 % · 5 s
→ LLO-2
DS-04
Load control
≤ 1 s
≥ 4 channels · ≥ 3 levels
→ LLO-3

## Slide 23
EE499 · Team 16 · Smart Home Energy Management
26
04 · DESIGN REQUIREMENTS
Design specifications (2/2)
DS-05
Reconnection
5 s
Stable margin · highest first
→ LLO-3 · 6
DS-06
Cost & budget
±5 %
Alerts 50 · 80 · 100 %
→ LLO-4
DS-07
User warnings
≤ 5 s
7-day log · 1 h
→ LLO-2 · 5
DS-08
Fail-safe
≤ 2 s
De-energize · override
→ LLO-6

## Slide 24
REQUIRED BEHAVIOUR · DS-03 / DS-07
Abnormal-operation warning
120 / 80 %
of baseline
≥ 5 s
persistence
≥ 90 %
detection rate
≤ 5 s
to warn

## Slide 25
EE499 · Team 16 · Smart Home Energy Management
27
04 · DESIGN REQUIREMENTS
Realistic constraints
C-01 · BUDGET
≤ 1,000 SAR
C-02 · SCHEDULE
Before the deadline
C-03 · SCOPE
Single-phase
C-04 · LAB POWER
≤ 2 kW
C-05 · APPLIANCES
No modification
C-06 · SAFETY
Supervised lab
C2 to c4, c3 to c2

## Slide 26
EE499 · Team 16 · Smart Home Energy Management
28
04 · DESIGN REQUIREMENTS
Engineering standards
IEC
IEC 60730-1:2022
Automatic controls
IEC
IEC 62053-21:2020
Energy-metering accuracy
SBC
SBC 401 (2024)
Wiring & protection
GSO
Gulf Technical Regulation
Low-voltage equipment
Engineering and safety guidance — certification out of scope.
Add icons for every standard

## Slide 27
EE499 · Team 16 · Smart Home Energy Management
29
04 · DESIGN REQUIREMENTS
Realistic assumptions
Normal operation at baseline
Test loads available
Lab + calibrated instruments
Protected, grounded supply
Up-to-date tariff
Correct user inputs

## Slide 28
EE499 · Team 16 · Smart Home Energy Management
30
04 · DESIGN REQUIREMENTS
Project deliverables
D-1
Prototype
D-2
Test bench
D-3
Firmware & UI
D-4
Validation results
D-5
Documentation

## Slide 29
Visibility. Priority. Safety.
A need — not a luxury.
Thank you — questions?
Team 16 · Ali Khudhayr · Mohammad Kassem · Omar Baflah

## Slide 30
REQUIRED BEHAVIOUR · DS-04 / DS-05
Priority control in action
≤ 1 s
shedding starts
≥ 4 · ≥ 3
channels · priorities
5 s
stable margin
3 s
motor restarts
Thank you — questions?